## Slide 1: Verifying the integration of PhreeqcRM with 2DSoil Model by Simulating Cation Exchange In a Soil Column
Presentation Layout:
Introduction
Model Details

## Slide 2: Verification Exercise Simulating Cation Exchange In a Soil Column
Geochemical model PhreeqcRM has been coupled with 2DSoil model resulting in an Advective-Dispersive-Reactive Transport (ADRT) model
I have performed a verification exercise to check its performance by simulating a cation exchange problem with 2DSoil-PhreeqcRM and comparing its results against those obtained from the in-built transport module in Phreeqc
  This in-built transport module can simulate ADRT under saturated conditions
In this verification exercise, I have simulated cation exchange in a soil column where an infiltrating solution laden with Ca2+ cation leads to the replacement of the already existing Na+ and K+ cations
  Same ADRT conditions have been maintained in both simulations
Why Cation Exchange Problem?: Because it is an agriculturally relevant problem as explained later

## Slide 3: Verification Exercise Simulating Cation Exchange In a Soil Column
Motivation:
Similar approach has been followed by Jacques and Šimůnek (2005) for verifying the integration of Phreeqc with Hydrus 1D
Scope of Additional Exercises:
Other exercises such as kinetics or redox reactions can also be performed for further verification

## Slide 4: Introduction To Cation Exchange
Excerpts from Phreeqc Database
Soil (clay and organic matter) is negatively charged and has a tendency to hold cations such as Ca2+ , Na+ , K+ and NH4+
Different cations are held by exchanger with different strengths
  I+ + X- IX; logK = Y
    Where I+ is a cation and X- is exchanger site, logK is the selectivity coefficient which characterises the strength of an exchange site to hold a cation.
    Higher the logK for a cation translates to higher holding strength.
      For Na+ : logK = 0.0
      For K+ : logK = 0.7
      For Ca2+ : logK = 0.8
    An existing pre-exchanged cation can be replaced by another cation. This phenomenon is known as cation exchange
    For example, if a soil column initially contains Na+ and K+, an infiltrating solution containing Ca2+ will first replace Na+ in the soil first and will then replace K+ on the basis of their relative logK value
      This dislodging of Na+ and K+ cations is called elution

## Slide 5: Model Characteristics (common to both simulations)
Model domain dimensions: A 100cm long soil column
Flow Conditions: 1-D saturated steady state flow
Flow Direction: From top to bottom
Geo-chemical composition and Solute related Boundary Conditions
  Each cell/node in the column initially contains 1.1 milli moles of exchanger (X)
  Initially, each cell/node has 1.0 mmols Na+ , 0.2 mmols K+ and 1.2 mmols NO3- . This is equivalent to 1 mmol of NaNO3 and 0.2 mmol of KNO3
  Prescribed concentrations at the top surface of the soil column are 0.6 mmols of Ca2+ and 1.2 mmols Cl- i.e. 0.6 mmols CaCl2.
    Flow carries Ca2+ and Cl- to the lower sections of the soil column leading to the elution of Na+ and K+

## Slide 6: Simulations based on 2DSoil-PhreeqcRM
Grid and Flow Conditions:
  Length of simulated column: 100 cm
  Grid size: 1 cm vertically
  Soil Characteristics:
    KS = 10 cm/day ; = 0.2 ; D = 2 cm ; diffusion coefficient = 0.0
  Initial Conditions:
    Initialized with = at all nodes
  Flow related boundary conditions:
    Prescribed a constant head of 1 cm at the top of the domain
    Free drainage conditions (unit gradient) at the bottom
      For saturated conditions, Darcy vel. = KS (see https://www.pc-progress.com/forum/viewtopic.php?t=98)
      Pore vel. = KS/ = 10/0.2 cm/day = 50 cm/day
  Time step = 1 hour (Default value)
  Simulated duration = 5 days (or 432000 seconds)

## Slide 7: Model Characteristics for 2DSoil-PhreeqcRM
Initialize solute and X concentrations and print outputs
  Solute Transport Conditions:
    Number of solutes = 5 : Ca2+ , Cl- , Na+ , K+ and NO3-
    Prescribed constant solute concentrations at the top most nodes:
      Ca2+ = 24.0 mg/l (= 0.6 mmol/l; GFW = 40 gm)
      Cl- = 42.6 mg/l (= 1.2 mmol/l; GFW = 35.45 gm)
    Initial concentrations of Na+ , K+ and NO3- are defined by PhreeqcRM input file (refer Figure (a) in the panel on the right)
  Solute concentrations were prescribed using fertigation module (added last month to the TF repository)
    This module reads the type of solute BC and the prescribed values (VarBS)
    fertigation module also prints out the concentrations of solutes in mmols
  1.1 millimoles of X is defined for all nodes using cell 0 as initial condition (refer Figure (b) in the panel on the right)
Excerpts from PhreeqcRM input file
(a)
(b)

## Slide 8: Model Characteristics for Phreeqc’s Transport Module
Grid and Flow Conditions:
  Advective dispersive transport is simulated using a shift based method where water in one cell is shifted to another in a user defined time step
  Model domain is composed of 100 cells with each having a length of 1 cm (total length of domain = 1 m)
    A single shift equates to downward movement of soil water by 1 cm
  Time step calculations
    simulated pore velocity in 2DSoil-PhreeqcRM based simulations = 50 cm/day
    To obtain similar pore velocity : time step = (Length travelled in a shift)/(Pore Vel)
      Time step = 1cm/(50 cm/86400 seconds) = 1728 seconds (28.8 minutes)
  Number of Shifts = Simulated duration/ time step = 432000/1728 = 250 shifts
  Dispersivity = 2 cm (same as that in 2DSoil-PhreeqcRM based simulations)

## Slide 9: Model Characteristics for Phreeqc’s Transport Module
Initialize solute concentrations and print outputs
  Solute Transport Conditions:
    Prescribed constant solute concentrations at the top most node (refer Figure (b) in the right panel)
      Ca2+ = 24.0 mg/l (=0.6 mmol/l)
      Cl- = 42.6 mg/l (=1.2 mmol/l)
    Initial concentrations of Na+ , K+ and NO3- are defined by Phreeqc input file (refer Figure (b) in the right panel)
  Solute concentrations were prescribed using fertigation module (added last month to the TF repository)
  Solute concentrations are printed out by the fertigation module
Excerpts from PhreeqcRM input file
(a)
(b)

## Slide 10: Results
In the next few slides I have presented the following results obtained from 2DSoil-PhreeqcRM and Phreeqc’s in-built transport module:

## Slide 11: Comparison of Simulated Concentration Profiles : Ca2+ and Na+
Chart: Comparison of Ca2+ Concentrations after 1 Day
Chart: Comparison of Ca2+ Concentrations after 2 Days
Chart: Comparison of Ca2+ Concentrations after 3 Days
Chart: Comparison of Ca2+ Concentrations after 4 Days
Chart: Comparison of Na+ Concentrations after 1 Day
Chart: Comparison of Na+ Concentrations after 2 Days
Chart: Comparison of Na+ Concentrations after 3 Days
Chart: Comparison of Na+ Concentrations after 4 Days
Day 1
Day 2
Day 3
Day 4
Ca2+
Na+

## Slide 12: Comparison of Simulated Concentration Profiles: Ca2+ and K+
Chart: Comparison of Ca2+ Concentrations after 1 Day
Chart: Comparison of Ca2+ Concentrations after 2 Days
Chart: Comparison of Ca2+ Concentrations after 3 Days
Chart: Comparison of Ca2+ Concentrations after 4 Days
Day 1
Day 2
Day 3
Day 4
Chart: Comparison of K+ Concentrations after 1 Day
Chart: Comparison of K+ Concentrations after 2 Days
Chart: Comparison of K+ Concentrations after 3 Days
Chart: Comparison of K+ Concentrations after 4 Days
Ca2+
K+

## Slide 13: Comparison of Simulated Concentration Profiles: Cl- and NO3-
Day 1
Day 2
Day 3
Day 4
Cl-
NO3-
Chart: Comparison of Cl- Concentrations after 1 Day
Chart: Comparison of Cl- Concentrations after 2 Days
Chart: Comparison of Cl- Concentrations after 3 Days
Chart: Comparison of Cl- Concentrations after 4 Days
Chart: Comparison of NO3- Concentrations after 1 Day
Chart: Comparison of NO3- Concentrations after 2 Days
Chart: Comparison of NO3- Concentrations after 3 Days
Chart: Comparison of NO3- Concentrations after 4 Days

## Slide 14: Discussion of Results
Cation Exchange:
  Na+ is held weakly by the exchanger due to its lower selectivity coefficient (logK = 0) leading to it being simply flushed out with the flow
  K+ is held relatively stronger by exchanger in the soil due to a higher selectivity coefficient (logK = 0.7)
    This leads to accumulation as it is eluted from the exchanged sites. This accumulation is elucidated by the peaks in the concentration profiles
Anion dynamics:
  Both anions and exchange sites are negatively charged and do not interact due to repulsion

## Slide 15: Conclusion and scope of additional exercises
Conclusion:
  Results obtained from 2DSoil-PhreeqcRM based simulations show good agreement with those obtained from the in-built transport module in Phreeqc
Scope of additional exercises:
  Other agro-geochemical scenarios can be simulated
    One of them is the simulation of experimental studies conducted at UNL